## Slide 1: Module 3
Step-by-Step Execution of Simple Programs

## Slide 2: Learning Objectives
Understand how simple programs execute step-by-step
Interpret instruction flow diagrams
Explain the role of registers in computation
Connect instructions to hardware-level actions

## Slide 3: What Is a Program?
A program is a sequence of instructions
Each instruction tells the CPU to perform a specific task
Instructions are executed sequentially (by default)

## Slide 4: Basic Execution Cycle
Fetch → Decode → Execute
  Fetch instruction from memory
  Decode instruction
  Execute instruction
  Move to the next instruction

## Slide 5: Step-by-Step Execution Example
ARM Assembly Program
  MOV R1, #5
  MOV R2, #3
  ADD R3, R1, R2
Execution
  Load 5 into R1
  Load 3 into R2
  Add R1 + R2 → store in R3

## Slide 6: Instruction Flow Diagram
Visual representation of execution steps
Shows control flow and data movement
FETCH the instruction and any data from main memory
DECODE the instruction (i.e., convert the instruction into a language the CPU understands)
EXECUTE the instruction (i.e., complete the instruction)

## Slide 7: What are Registers?
Small, fast storage inside the CPU
Hold data temporarily
Used during instruction execution
Examples
  R1, R2, R3
  Program Counter (PC)
General Purpose Registers | R0
 | R1
 | R2
 | R3
 | R4
 | …
Stack | SP
Program Counter | PC

## Slide 8: Types of Registers General and SP
General Purpose Registers
  R0 to R12
  Contain either data or addresses
Stack Pointer (SP)
  R13
  Points to the top element of the stack
General Purpose Registers | R0
 | R1
 | R2
 | R3
 | R4
 | …
Stack | SP
Program Counter | PC

## Slide 9: Types of Registers PC
Program Counter (PC)
  Points to the next instruction to be fetched
  The CPU fetches the instruction and then increments PC
General Purpose Registers | R0
 | R1
 | R2
 | R3
 | R4
 | …
Stack | SP
Program Counter | PC

## Slide 10: Register Operations
Common operations
  Load: move data into register
  Store: move data to memory
  Add/Subtract: arithmetic operations
Example (ARM Assembly)
ADD R0, R1, R2

## Slide 11: Instruction = Hardware Action
Each instruction triggers hardware-level operations
  Data transfer between registers
  ALU computation
  Memory access
Example
  ADD → ALU performs addition
Image Source: https://erik-engheim.medium.com/what-the-heck-is-a-micro-operation-e991f76209e

## Slide 12: Micro-Operations
Instructions break into smaller steps
Example (ADD):
  Read R1
  Read R2
  ALU computes sum
  Store result in R3
Image Source: https://erik-engheim.medium.com/what-the-heck-is-a-micro-operation-e991f76209e

## Slide 13: Control Unit Role
Directs all operations
Generates control signals
Ensures correct sequence of execution
Image Source: https://erik-engheim.medium.com/what-the-heck-is-a-micro-operation-e991f76209e

## Slide 14: Putting It All Together
Program Execution:
  Instructions → Micro-operations → Hardware actions
Registers store intermediate data
Control unit manages flow
Image Source: https://erik-engheim.medium.com/what-the-heck-is-a-micro-operation-e991f76209e

## Slide 15: Summary
Programs execute step-by-step
Instruction flow diagrams visualize execution
Registers are essential for fast computation
Every instruction maps to hardware activity

## Slide 16: Discussion/Questions
What happens if registers are limited?
How does branching affect flow?
Can instructions execute in parallel?