## Slide 1: Module 4
Verilog, ALU, and Simulation

## Slide 2: Learning Objectives
Understand basic Verilog syntax and module structure
Design and implement a simple ALU
Perform simulation and interpret waveforms

## Slide 3: What is Verilog?
Hardware Description Language (HDL)
Used to model digital systems
Describes behavior and structure of hardware

## Slide 4: Verilog Module Basics
Fundamental building block
Defines inputs, outputs, and internal logic

## Slide 5: Data Types and Signals
Type | Represents | Example | Synthesizable?
Nets (wire) | Physical connections between hardware elements | wire a; | Yes
Variables (e.g., reg) | Storage elements holding values until next assignment | reg q; | Yes (if used properly)
Input/Output Declarations

## Slide 6: Continuous vs. Procedural Assignments
assign
Continuous (combinational)
always block
Procedural (sequential or combinational)

## Slide 7: Continuous Assignment (Combinational)
Uses assign
Always active (updates automatically when inputs change)
Only works with wire
Key Idea:
  This is like a direct connection
  Hardware is always ‘on’ and updating

## Slide 8: Procedural Assignment
Uses always
Executes when triggered by the sensitivity list
Uses reg type
Key Idea:
  This behaves like a block of instructions that runs when inputs change

## Slide 9: Continuous vs. Procedural Table
Feature | Continuous (assign) | Procedural (always)
Type | Combinational only | Combinational + Sequential
Signal type | wire | reg
Execution | Always active | Triggered
Example use | Simple logic | ALUs, registers

## Slide 10: ALU Overview
Arithmetic Logic Unit (ALU)
Performs operations like add, subtract, AND, OR
Core component of CPUs

## Slide 11: ALU Inputs and Outputs
Inputs: A, B (operands)
Control: opcode (select operation)
Output: result

## Slide 12: ALU Considerations
Bit width (8-bit vs. 32-bit)
  8-bits in this example
Signed vs. unsigned
Overflow and flags
  Future extension

## Slide 13: Simulation = Testing
Simulation is how we test hardware
Equivalent to unit testing in software
Run before building real hardware

## Slide 14: Why Simulation Matters
Catch bugs early
Faster than hardware debugging
No risk of damaging hardware

## Slide 15: Introduction to Testbenches
Special Verilog modules for testing
No inputs/outputs
Drive signals into your design

## Slide 16: Testbench = Automated Testing
Apply multiple test cases automatically
Repeatable and scalable
Key mindset:
design → test → debug → repeat

## Slide 17: Example Testbench

## Slide 18: Simulation Tools
ModelSim
Vivado
Icarus Verilog
Workflow
  Compile → Run → Analyze

## Slide 19: Waveform Analysis
Signals plotted over time
Shows how outputs respond to inputs

## Slide 20: What to Look For in Waveforms
Correct output values
Timing alignment
Opcode changes vs. result changes

## Slide 21: Debugging with Waveforms
Compare expected vs. actual behavior
Identify incorrect logic or timing
Check transitions and glitches

## Slide 22: Find the Bug
Assume a version of the previous code was used but there is a bug in this version

## Slide 23: The Bug
1010 1010 (0xaa) | 1100 1100 (0xcc) = 1110 1110 (0xee)
But the waveform shows 0x66 (0110 0110) at 5ns
Something must be wrong with the bitwise OR in this case

## Slide 24: Fixing the code
Code with a Bug
Fixed Code

## Slide 25: Re-run Waveform Analysis
Fixed!

## Slide 26: Putting It All Together
Write
Write Verilog module (design)
Write
Write testbench (tests)
Run
Run simulation (execute tests)
Analyze
Analyze waveforms (debug)

## Slide 27: Big Idea
Hardware design is NOT guess-and-check
It is systematic testing and verification
Simulation is your primary tool

## Slide 28: Summary
Verilog defines hardware behavior
ALU performs core operations
Testbenches automate testing
Waveforms help debug and verify designs

## Slide 29: Discussion/Questions
How would you add multiplication to the ALU?
What happens if you forget a test case?
Why is simulation critical before hardware?